## Slide 1
Modeling of Inverted Drift Tube Design for Classification of Sub-micrometric sized Particles at Atmospheric Pressure
October 19th 2016
Minal Nahin and Carlos Larriba Andaluz
A Kanomax Project

## Slide 2
Introduction
    Drift Tube requirements from Kanomax
    Design Concept for the Inverted Drift Tube
Modeling of Drift Tube
    Key Parameters
    Stopping the ions
    Arising Problems
New Strategies
    “Intermittent Push” Flow
    “Stopping Potential”
Instrument Characteristics
    Resolution
    Resolving power
Next Steps

## Slide 3
Initial Model Design and Characteristics:
  Fast Electrical Mobility Characterization System
  Wide Range of Mobilities (Diameters) 0.3nm<D<100nm
  Small device (<50cm)
  Room Pressure
  Can be coupled to a CPC (or an electrometer)
  High Resolution (and resolving power)
  Has to Compete against well established DMAs

## Slide 4
Initial Concept of Inverted Drift Tube (Comparison to regular Drift Tube)
  The Inverted Tube consists of two Forces: Electric Field and Drag Force.
  The Electric Field is directly proportional to axial distance x but negative in direction.
  There is a constant velocity flow, vgas, in the axial direction.
  At some point in the Drift Tube, the drift velocity, vdrift, will be equal to vgas.
  When this occurs, the particle is trapped inside the Inverted Drift Tube.
E
vgas
Field Strength
Axial Distance
vgas = vdrift = ZE
Lower Mobilities require Higher Fields!!!
E
vdrift = ZE
Constant Electric Field pushes the ions through
Field Strength
Axial Distance
REGULAR DRIFT TUBE
INVERTED DRIFT TUBE
Particles are stopped at some point in the Tube when:
Gas

## Slide 5
Nanoparticles of different Mobilities are stopped at their required Fields using SDS model.
Particles diameters shown range from 20 to 120 nm.
PROBLEMS THAT ARISE:
  When nanoparticles are stopped, radial fields push nanoparticles to walls of the cylinder. As particles migrate to cylinder walls, they do not follow constant field lines, but constant Ex lines. Smaller Particles are lost before large are stopped.
  Flow field, Vgas, is not uniform
How do we collect particles?
vgas
Constant Field Lines
Ex1
Ex2=Ex1
Er1
Er2>Er1
E

## Slide 6
The flow field is not uniform due boundary layer formation inside IDT
The flow profile is parabolic
Particles of same mass over charge have different velocities
Big disadvantage for resolution
How can we maintain same velocity for same mass over charge particles ?
Particles are mostly at the center
keep the center velocity constant for a profile

## Slide 7
  Increased the velocity
  Introduced annulus flow
  Introduced mesh at the inlet and out flow of IDT to make profile flat.
Flow profile from CFD simulation in steady state condition:
Profile corresponding to the blue lines shown in the CAD model
Flow

## Slide 8: Method of Separation First Approach

## Slide 9
Field Strength,
Velocity
Axial Distance
  First Approach: “Intermittent Push Flow”
  Lower the field in subsequent pushes guiding particles through the drift tube
Field Strength
vgas
Velocity
At center

## Slide 10
  First Approach: “Intermittent Push Flow”.
  Particles are modeled using Statistical Diffusion Simulations.
  Arrival Times of Particles can be easily inferred Analytically.

## Slide 11
  First Approach: “Intermittent Push Flow”.
  Resolution of particles as a function of arrival time distributions .
  Arrival time distributions of sets of 100 particles are studied with Statistical Diffusion Simulations.
R~182
R~487
R~750
R~961
Chart: Resolution for 5E6 mass (20.59 nm dia)
| 4.1193499999999998 | 4.1253500000000001 | 4.1313500000000003 | 4.1373499999999996 | 4.1433499999999999 | 4.1493500000000001 | 4.1553500000000003 | 4.1613499999999997 | 4.1673499999999999 | 4.1733500000000001 | 4.1793500000000003
 | 0 | 2 | 2 | 14 | 27 | 29 | 14 | 9 | 2 | 1 | 0
Chart: Resolution for 6e7 amu mass (47.14 nm dia)
| 2.3741099999999999 | 2.47601 | 2.5779100000000001 | 2.6798099999999998 | 2.5817100000000002 | 2.5836100000000002 | 2.5855100000000002 | 2.5874100000000002 | 2.5893100000000002 | 2.5912100000000002
 | 0 | 0 | 12 | 15 | 32 | 26 | 13 | 2 | 0 | 0
Chart: Resolution for 1e9 mass (120.42 nm dia)
| 2.3363299999999998 | 2.3370299999999999 | 2.3377300000000001 | 2.3384299999999998 | 2.3391299999999999 | 2.3398300000000001 | 2.3405300000000002 | 2.3412299999999999 | 2.3419300000000001 | 2.3426300000000002 | 2.3426300000000002
 | 0 | 0 | 7 | 16 | 27 | 26 | 13 | 9 | 2 | 0 | 0
Chart: Resolution for 3e8 amu mass (80.61 nm dia)
| 2.38917 | 2.3903699999999999 | 2.3915700000000002 | 2.3927700000000001 | 2.3939699999999999 | 2.3951699999999998 | 2.3963700000000001 | 2.39757 | 2.3987699999999998 | 2.3999700000000002
 | 0 | 0 | 4 | 16 | 31 | 29 | 16 | 4 | 0 | 0

## Slide 12
  First Approach: “Intermittent Push Flow”.
  Why do we have such a high resolution ?
  Diffusion “Auto-Correction” as particles fly through drift tube.
  Only when the Electric Field is set to low values, particles freely diffuse (very small relative times of diffusion compared to total flight time).
  Resolution & resolving power can be enhanced by tuning intermittent pushes.
Field Strength
Axial Distance
ZE=Vgas
Stable
vgas
ZE<Vgas
Particle is pushed forward
ZE>Vgas
Particle is pushed backwards

## Slide 13
  Resolution for two close particles might be very high (in our case for larger particles) but it might not be helpful for separation.
  Also we can always tune electric field pushes to get high resolution for a specific particle size, so we cannot define an exclusive resolution. Is there a different easy to define resolution?
  Define how well the peaks can be distinguished : resolving power!
gHW
W
If resolving power is zero then then there is no gap at the half width !
So, we conclude:
If resolving power > 0.2 peaks are separable
If resolving power < 0.2 peaks are not separable

## Slide 14
120.42 nm
114.07 nm
98.06 nm
95.57 nm
82.70 nm
80.61 nm
56.81 nm
55.89 nm
Ions are within 5.27 %
RP = 1.02
Ions are within 2.54 %
RP = 0.46
Ions are within 2.53 %
RP = 0.51
Ions are within 1.62 %
RP = 0.56
47.91 nm
47.14 nm
33.22 nm
32.69 nm
20.93 nm
Ions are within 1.61 %
RP = 0.68
Masses are within 1.60%
RP = 1.16
Ions are within 1.62 %
RP = 1.42
20.59 nm
Separation of very close masses is possible if the masses are small (diameter small)
Resolving power is inversely proportional to diameter or mass

## Slide 15
  First Approach: “Intermittent Push Flow”.
  Consider the resolution of DMA is 10
  DMA with resolution 10 can not distinguish 44~50 nm diameter ions
Inverter Drift Tube
DMA
Chart: 
| 37.712000000000003 | 40.069000000000003 | 42.426000000000002 | 44.783000000000001 | 47.14 | 49.497 | 51.853999999999999 | 54.210999999999999 | 56.567999999999998
 | 0.00080919 | 0.007601 | 0.037648 | 0.098326 | 0.13541 | 0.098326 | 0.037648 | 0.007601 | 0.00080919
 | 1.2551e-07 | 3.0712e-05 | 0.0027646 | 0.09155 | 1.1153 | 4.9984 | 8.241 | 4.9984 | 1.1153 | 0.09155 | 0.0027646 | 3.0712e-05 | 1.2551e-07
Chart: 
| 37.712000000000003 | 40.069000000000003 | 42.426000000000002 | 44.783000000000001 | 47.14 | 49.497 | 51.853999999999999 | 54.210999999999999 | 56.567999999999998
 | 0.00080919 | 0.007601 | 0.037648 | 0.098326 | 0.13541 | 0.098326 | 0.037648 | 0.007601 | 0.00080919
 | 1.2551e-07 | 3.0712e-05 | 0.0027646 | 0.09155 | 1.1153 | 4.9984 | 8.241 | 4.9984 | 1.1153 | 0.09155 | 0.0027646 | 3.0712e-05 | 1.2551e-07

## Slide 16: Second Approach

## Slide 17
  Second Approach: “Stopping Potential Separation”
  A field is fixed on the drift tube so as to stop only one mobility
Constant Field Applied
  When a constant Field is applied, particles with larger mobilities are pushed to the entrance as ZE>Vgas ,while particles with smaller mobilities are pushed to the exit as ZE< Vgas.
vgas

## Slide 18
  Second Approach: “Stopping Potential Separation”
  A field is fixed on the drift tube so as to stop only one mobility
  Red Markers Correspond to 1 second each.
  Arrival time separation for 1% mass differential: 10 seconds (for a 47nm particle)

## Slide 19
  Second Approach: “Stopping Potential Separation”
  Separation Possibilities? Can we separate 0.07% in diameter? (55.89 nm & 55.93 nm)
  Theoretically: Yes we can! What happens when the Field is not exactly known?
  When the Field is not exactly known a small RF Field can be used to stop a range of mobilities.

## Slide 20
  CONCLUSIONS
  We have Designed and Modeled an Inverted Drift Tube which is small (12 cm) fast (~5s for a total sweep), has a high mass/diameter (>100nm) range and high Resolution and resolving power.
  The Drift Tube has 3 possible methods of operation:
    Particles could be collected at the walls with a fixed potential.
    Collect particles using a CPC or electrometer through “Intermittent push flow”.
    Use a Stopping potential to focus on a particle size (High Separation).
  The ideal situation shows very high resolutions in Arrival Time Distributions.
  Shows high resolving power specially for small particles
  FUTURE WORK
  Mathematical description of working principle inverted drift tube
  A prototype of the Drift Tube will be constructed

## Slide 21
  THANK YOU !!
  QUESTIONS?